## Slide 1: Tests of a 10cm by 10cm triple GEM detector
2015-06-08

## Slide 2
Detector (3/2/2/2 mm, 10cm by 10cm) is equipped with a 2D readout board, which has 4 Panasonic connectors.
A filter with 100kOhm*3/2.2nF*2 is at the HV input.
Put X-ray focus on one quadrant (with a 2 mm collimator), and connect 2 connectors with 128 strips combined for each. This signal is added together to pico-ameter.
Count rate, current on strips, spectrum can be recorded simultaneously.
Bottom of
3rd foil
Preamp.
Linear amp.
Scope
MCA
Discriminator
Scaler
Readout strips
(128*2)
Pico-Ameter
Setup description

## Slide 3
Threshold 50 mV
Background count rate is high, among which the cosmic ray count rate is about 200 Hz at highest tested voltage (~4260 V on drift).
Rate for X-ray (at 10kV/5uA) is measured. Plateau rate (~46kHz) starts at 660 uA through the divider. Comparing with the X ray, cosmic ray counts are very small (but they are subtracted).
Counting rate

## Slide 4
Spectra of X-ray at 10kV/5uA
Vd=3600V
I=664.5uA
Vd=3695V
I=682uA
Vd=3790V
I=699.5uA
Vd=3885V
I=717uA
Vd=3980V
I=734.55uA
Vd=4074V
I=752.1uA

## Slide 5
Spectrum peak vs. detector current
(X-ray at 10kV/5uA)
Statistic errors less than marker size

## Slide 6
Current measured from readout strips (Cosmic ray)
Vd=3980V,
I=734.5uA
Vd=4264V
I=787.1uA
Cosmic signals show currents of 0.04~0.09 nA
Bkg current at low voltage
Bkg current at high voltage

## Slide 7
Current measured from readout strips (X-ray at 10kV/5uA)
Vd=4122V
At each tested voltage point, current is stable! The above two plots are for the highest tested point (Vd=4122V).
Current on strip vs. current in divider is shown on the right.
Statistic errors less than marker size

## Slide 8
Gain curve

## Slide 9
Test of the X ray gun – voltage scan at 5 uA (Vd=3980V, I=734.5uA)
X Ray at 10 kV
X Ray at 16 kV
X Ray at 20 kV
X Ray at 24 kV
Peak shifts to the left and finally disappears as voltage increases!
Current on strips is monitored (next slide), did not go higher Xray voltage for the safe of the detector.

## Slide 10
X Ray at 10 kV
X Ray at 16 kV
X Ray at 20 kV
X Ray at 24 kV
Current reached ~0.47 uA !
Test of the X ray gun – voltage scan at 5 uA (Vd=3980V, I=734.5uA)

## Slide 11
Test of the X ray gun – voltage scan at 5 uA (Vd=3695V, I=682uA)
X Ray at 10 kV
X Ray at 20 kV
X Ray at 30 kV
X Ray at 40 kV
X Ray at 50 kV
pedestal peak
X ray bump

## Slide 12
Test of the X ray gun – current scan at 10 kV (Vd=3980V, I=734.5uA)
X Ray at 10 uA
X Ray at 30 uA
X Ray at 60 uA
X Ray at 90 uA
Again, peak shifts to the left as current increases!!

## Slide 13
X Ray at 10 uA
X Ray at 30 uA
X Ray at 60 uA
X Ray at 90 uA
Current reached ~350 nA at 90uA in X ray gun.
Test of the X ray gun – current scan at 10 kV (Vd=3980V, I=734.5uA)

## Slide 14
Spectrum peak vs. Xray current
Current through strips vs. Xray current
Test of the X ray gun (Vd=3980V, I=734.5uA)
Spectrum peak vs. Xray voltage
Current through strips vs. Xray voltage
Statistic errors less than marker size
Statistic errors less than marker size
Statistic errors less than marker size
Statistic errors less than marker size

## Slide 15
An explanation?:
->Consider a GEM detector’s energy resolution 16-18%, the RMS for 10keV X Rays is 1.6-1.8keV.
->When Xray gun voltage >=20kV, the energy spectrum is very wide. It has peaks of 8-15keV with gaps of ~2keV.
->So that the detector can not really “see” the peaks.